## Slide 1: Multi-core processors

## Slide 2: Processor development till 2004
Out-of-order
Instruction scheduling

## Slide 3: Why multi-core ?
Difficult to make single-core clock frequencies even higher – heat problems
Deeply pipelined circuits:
  heat problems, needs special cooling arrangements
  Intel’s NetBurst architecture was not continued
Many new applications are multithreaded
General trend in computer architecture (shift towards more parallelism)

## Slide 4: Why multi-core ?

## Slide 5: Single-core computer

## Slide 6: Single-core CPU chip
the single core

## Slide 7: Multi-core architectures
Replicate multiple processor cores on a single die.
Core 1
Core 2
Core 3
Core 4
Multi-core CPU chip

## Slide 8: Multi-core processor

## Slide 9: Multi-core CPU chip
The cores fit on a single processor socket
Also called CMP (Chip Multi-Processor)
core
1
core
2
core
3
core
4

## Slide 10: The cores run in parallel
core
1
core
2
core
3
core
4
thread 1
thread 2
thread 3
thread 4

## Slide 11: Within each core, threads are time-sliced (just like on a uniprocessor)
core
1
core
2
core
3
core
4
several threads
several threads
several threads
several threads

## Slide 12: Interaction with the Operating System
OS perceives each core as a separate processor
OS scheduler maps threads/processes to different cores
Most major OS support multi-core today: Windows, Linux, Mac OS X, …

## Slide 13: Instruction-level parallelism
Parallelism at the machine-instruction level
The processor can re-order, pipeline instructions, split them into microinstructions, do aggressive branch prediction, etc.
Instruction-level parallelism enabled rapid increases in processor speeds over the last 15 years

## Slide 14: Thread-level parallelism (TLP)
This is parallelism on a more coarser scale
Server can serve each client in a separate thread (Web server, database server)
A computer game can do AI, graphics, and a physics-related computation in three separate threads
Single-core superscalar processors cannot fully exploit TLP
Multi-core architectures are the next step in processor evolution: explicitly exploiting TLP

## Slide 15: General context: Multiprocessors
Multiprocessor is any computer with several processors
SIMD
  Single instruction, multiple data
  Modern graphics cards
MIMD
  Multiple instructions, multiple data
Lemieux cluster, Pittsburgh supercomputing center

## Slide 16: Multiprocessor memory types
Shared memory: In this model, there is one (large) common shared memory for all processors
Distributed memory: In this model, each processor has its own (small) local memory, and its content is not replicated anywhere else

## Slide 17: Multi-core processor is a special kind of a multiprocessor: All processors are on the same chip
Multi-core processors are MIMD: Different cores execute different threads (Multiple Instructions), operating on different parts of memory (Multiple Data).
Multi-core is a shared memory multiprocessor: All cores share the same memory

## Slide 18: What applications benefit from multi-core?
Database servers
Web servers (Web commerce)
Multimedia applications
Scientific applications, CAD/CAM
In general, applications with Thread-level parallelism (as opposed to instruction-level parallelism) are better supported
Each can run on its own core

## Slide 19: More examples
Editing a photo while recording a TV show through a digital video recorder
Downloading software while running an anti-virus program
“Anything that can be threaded today will map efficiently to multi-core”
BUT: some applications difficult to parallelize